## Slide 1: T-infinity: The Dependency Inversion Principle for Rapid and Sustainable Multidisciplinary Software Development
Matthew D. O’Connell, Cameron T. Druyor, Kyle B. Thompson, Kevin E. Jacobson,
W. Kyle Anderson, Eric J. Nielsen, Jan-Reneé Carlson, Michael A. Park, William T. Jones,
Robert T. Biedron, and Bil Kleb NASA Langley Research Center
Xinyu Zhang
Analytical Mechanics Associates, Inc.

## Slide 2: CFD 2030 Vision Report
“NASA should develop and maintain an integrated simulation and software development infrastructure to enable rapid CFD technology maturation.” - CFD 2030 Vision Report Programmatic Recommendation #2
We are attempting to guide new software development efforts and add benefits to existing software tools keeping this recommendation in mind.

## Slide 3: Motivation
Software should scale!
  Scale with computer resources. (Parallel Scalability)
  Scale with human resources. (Human Scalability)
Challenges:
  Problems are so complex, no one can be an expert in every aspect.
  Experts solving problems from a different domain of expertise is suboptimal.
Has someone else solved this software complexity problem?
Notes: Many advanced technologies exist, but are often not fully integrated.
Complex engineering challenges lead to complex solutions, and often complex software code bases.
Engineers, scientists, and programmers can’t be an expert in every aspect of the problem space.
To solve ever challenging problems we need experts to focus on their part of the problem that is within their expertise.
Whenever possible experts need to be able to ignore details from experts in other disciplines.
Our analysis and design software should enable, not inhibit, expert-scalability.

## Slide 4: Borrow from Software Engineering
SOLID Design Principles
  Single Responsibility Principle
    Software entities should have only one reason to change.
  Open Closed Principle
    Software entities should be open for extension, but closed for modification.
  Liskov Substitution Principle
    Subtypes must be substitutable for their base types.
  Interface Segregation Principle
    Clients should not be forced to depend on methods that they do not use.
  Dependency Inversion Principle
Dependency Inversion Principle
  High-level modules should not depend on low-level modules. Both should depend on abstractions.
  Abstractions should not depend on details. Details should depend on abstractions.

## Slide 5: Borrow from Software Engineering
Dependency Inversion Principle
  High-level modules should not depend on low-level modules. Both should depend on abstractions.
  Abstractions should not depend on details. Details should depend on abstractions.

## Slide 6: Direct Coupling
Low level detail
High level concept
Dependency
No!
Causes tight coupling,
hard to maintain,
high cognitive load.
A specific turbulence model
CFD Solver

## Slide 7: Dependency Inversion
Abstraction
High level concept
Dependency
Low level detail
Implements
Yes!
Forces modularity,
easy to extend,
lower cognitive load
Stress Tensor Closure
CFD Solver
Needs a
A specific turbulence model
Can Give

## Slide 8
Abstractions

## Slide 9
Plugins Implement Abstractions

## Slide 10
Applications Use Abstractions

## Slide 11
Applications Don’t “Know” About Plugins

## Slide 12
T-infinity is Only Abstractions

## Slide 13
Flexible Uses: Adapt Existing Data Structures
Legacy applications can adapt existing data structures to leverage desired features.
T-infinity interfaces are not a framework.

## Slide 14
Flexible Uses: Cohesive Orchestrating Applications
The interfaces are designed to be independent, yet collaborative.
The output of one interface is the input of another.
Orchestrating applications can be written without adapting data.

## Slide 15
Simple Application: Steady State CFD

## Slide 16
Simple Application: Steady State CFD
Inviscid Analysis
Fluid Solver: FUN3D
Visualization & Preprocessing: Parfait

## Slide 17
Simple Application: Steady State CFD

## Slide 18
Pick and choose: Overset

## Slide 19
Two domain overset:
Fluid Solver: HyperSolve (Prototype Finite Volume)
Domain Assembler: YOGA
Visualization & Preprocessing: Parfait
Pick and choose: Overset

## Slide 20
Pick and choose: Overset

## Slide 21
Pick and choose: Mesh Adaptation

## Slide 22
Mach Hessian to metric based adaptation.
Solver: SFE
Adaptation, Visualization, Preprocessing: Refine
Access to CAD via EGADS lite.
Pick and choose: Mesh Adaptation

## Slide 23
Pick and choose: Mesh Adaptation

## Slide 24
Pick and choose: Fluid Structures Interaction

## Slide 25
Static structural deflection
Solver: HyperSolve
Loads Transfer: FunToFem
Structural Solver: TACS
Volume mesh deformed: FUN3D libMeshDef
Visualization & Preprocessing: Parfait
Pick and choose: Fluid Structures Interaction

## Slide 26
Static structural deflection
Solver: HyperSolve
Loads Transfer: FunToFem
Structural Solver: TACS
Volume mesh deformed: FUN3D libMeshDef
Visualization & Preprocessing: Parfait
Pick and choose: Fluid Structures Interaction

## Slide 27
Pick and choose: Fluid Structures Interaction
Static structural deflection
Solver: SFE
Loads Transfer: FunToFem
Structural Solver: TACS
Volume mesh deformed: FUN3D libMeshDef
Visualization & Preprocessing: Parfait

## Slide 28
Pick and choose: Fluid Structures Interaction
Static structural deflection
Solver: SFE
Loads Transfer: FunToFem
Structural Solver: TACS
Volume mesh deformed: FUN3D libMeshDef
Visualization & Preprocessing: Parfait

## Slide 29
Pick and choose: Fluid Structures Interaction

## Slide 30: Summary of Current Status
Finalizing Interfaces for solving steady state problems on vertex based unstructured grids.
Reference plugin implementations exist for:
  Mesh Pre-processing
  Mesh Adaptation
  Multiscale Metric Calculation
  Loads Transfer
  Fluid Solver
  Structural Solver
  Overset Domain Assembler
  Mesh To Mesh Interpolation
  Mesh Deformation
  Visualization
A plugin adapter is being written for FUN3D and VULCAN.
Interfaces and reference implementations for cell centered unstructured meshes are still under construction.

## Slide 31: Thank you!
Revolutionary Computational Aerosciences and Hypersonics Technology Project for funding this effort.
And to those who have shared feedback!

## Slide 32: Backup

## Slide 33: Dependency Inversion for Research
There is a clear separation from application developers using an interface, and research teams looking to implement it.
Independent research teams can work on their own implementation, but by following the set interface they can all be interchanged for comparison.
Technology improvements can be developed and tested in isolation without worrying about the complexity of the software that surrounds it.
When the time comes, it is trivial to integrate that new technology into a larger body of work.